## Slide 1: マルチエージェント強化学習を用いた自律分散型マイクログリッドのデザイン Design of Autonomous Decentralized Microgrids Using Multi-Agent Reinforcement Learning
M2 Morita Yudai
Weekly seminar @Nakata Lab.

## Slide 2
1. Introduction and background
2. Objective
3. Methodology
3.1 Step 1: Data collection
3.1.1 Data (demand, PV supply, wholesale price)
3.1.2 Car usage survey → Car usage data
3.1.3 Technology parameter (battery charge/discharge speed limit, efficiency)
3.2 Step 2: Model construction
3.2.1 Generate agent
3.2.2 Design P2P energy trading model
3.3 Step 3: Train agents
3.3.1 Q table
3.3.2 Reward
4. Results and analysis
5. Summary and future work
CONTENT

## Slide 3
1. Introduction and background
2. Objective
3. Methodology
3.1 Step 1: Data collection
3.1.1 Data (demand, PV supply, wholesale price)
3.1.2 Car usage survey → Car usage data
3.1.3 Technology parameter (battery charge/discharge speed limit, efficiency)
3.2 Step 2: Model construction
3.2.1 Generate agent
3.2.2 Design P2P energy trading model
3.3 Step 3: Train agents
3.3.1 Q table
3.3.2 Reward
4. Results and analysis
5. Summary and future work
CONTENT

## Slide 4
1. Introduction and background
Conventional structure
Electric companies in each region
Generation
Transmission
Distribution
Retail
Consumers
Supply obligations, regional monopolies Price regulation based on the full-cost method
Current structure (2016～)
TSO
DSO
Legal Separation
←
Electric companies
Generation
Generation
Generation
Wholesale Market(JEPX)
Retailer
Retailer
Retailer
Prosumer
FIT
FIT
FIP
Consumer
Consumer
FIP
Generation
Retail
Consumer
Each consumers/prosumers can choose appropriate Energy Retailer
一般財団法人 新エネルギー財団 電力市場の概要(その1)

## Slide 5
1. Introduction and background
[1] https://www.deloitte.com/nl/en/Industries/energy/blogs/peer-to-peer-energy-trading.html
[2] Chausov, Igor & Burdin, Ilya & Rybushkina, Alena & Ermolaev, Kirill & Kholkin, Dmitry. (2021). Internet of distributed energy architecture. Version 2.0.
Comparison of the principles of arrangement of centralized and decentralized energy systems [2]
・Increasing need for electricity in consumer’s everyday life, such as electrification of mobility
・Increasing decentralized and intermittent renewable electricity generation
The current system is struggling to deal with these developments, and this leads to higher energy bills, increased investment costs, and more challenges for the DSOs and TSO.[1]

## Slide 6
1. Introduction and background
[1] https://www.enecho.meti.go.jp
[2] https://www.jepx.jp/electricpower/market-data/spot/
[3] https://app.electricitymaps.com
Trends in renewable energy adoption in Japan [1]
JEPX spot price (30 min resolution) [2]
Energy mix of Japan (2024/5/8 ～2024/5/9) [3]
Chart: annual production [TWh]
| 2011 | 2022 | 2030 (target)
non renewable | 974.4 | 789.5 | 575.95
hydro | 84.825 | 76.9 | 98
biomass | 16.3125 | 37.1 | 47
solar | 4.35 | 92.6 | 146
wind | 4.35 | 9.3 | 51
geothermal | 2.175 | 3 | 11
9.2 %
14~16 %
Chart: 2011/4/1~2011/4/30
Chart: 2022/4/1~2022/4/30
Solar
・ Rooftop is considered as a location for installing further solar panels. [1]
・ Volatility in electricity wholesale prices within a day increased.
・ Up to approx.50% of electricity comes from solar panels on sunny days.
In this context, a decentralized energy system has worth being studied for further usage of Distributed Energy Resources (DERs).

## Slide 7
1. Introduction and background
Conventional structure
Electric companies in each region
Generation
Transmission
Distribution
Retail
Consumers
Supply obligations, regional monopolies Price regulation based on the full-cost method
Current structure (2016～)
TSO
DSO
Legal Separation
←
Electric companies
Generation
Generation
Generation
Wholesale Market(JEPX)
Retailer
Retailer
Retailer
Prosumer
FIT
FIT
FIP
Consumer
Consumer
FIP
Generation
Retail
Consumer
Each consumers/prosumers can choose appropriate Energy Retailer
一般財団法人 新エネルギー財団 電力市場の概要(その1)

## Slide 8
1. Introduction and background
Conventional structure
Electric companies in each region
Generation
Transmission
Distribution
Retail
Consumers
Supply obligations, regional monopolies Price regulation based on the full-cost method
Future structure (20XX～)
TSO
DSO
Legal Separation
←
Electric companies
Generation
Generation
Generation
Wholesale Market
Prosumer
Prosumer
Prosumer
Generation
Prosumer
一般財団法人 新エネルギー財団 電力市場の概要(その1)
Peer to Peer energy trading
An Autonomous Decentralized system is required!

## Slide 9
1. Introduction and background
2. Objective
3. Methodology
3.1 Step 1: Data collection
3.1.1 Data (demand, PV supply, wholesale price)
3.1.2 Car usage survey → Car usage data
3.1.3 Technology parameter (battery charge/discharge speed limit, efficiency)
3.2 Step 2: Model construction
3.2.1 Generate agent
3.2.2 Design P2P energy trading model
3.3 Step 3: Train agents
3.3.1 Q table
3.3.2 Reward
4. Results and analysis
5. Summary and future work
CONTENT

## Slide 10
The main objective is to propose an autonomous decentralized P2P energy trading system, and investigate its impact to both prosumers and energy grid.
Considering 2 scenarios:
1. Prosumers without P2P energy trading. (future coming consequence)
2. Prosumers community with P2P energy trading. (proposed)
2. Objective

## Slide 11
The main objective is to propose an autonomous decentralized P2P energy trading system, and investigate its impact to both prosumers and energy grid.
Considering 2 scenarios:
1. Prosumers without P2P energy trading. (future coming consequence)
➤Constructing the model…
2. Prosumers community with P2P energy trading. (proposed)
➤On training
2. Objective

## Slide 12
1. Introduction and background
2. Objective
3. Methodology
3.1 Step 1: Data collection
3.1.1 Data (demand, PV supply, wholesale price)
3.1.2 Car usage survey → Car usage data
3.1.3 Technology parameter (charge/discharge speed limit, efficiency)
3.2 Step 2: Model construction
3.2.1 Generate agent
3.2.2 Design P2P energy trading model
3.3 Step 3: Train agents
3.3.1 Q table
3.3.2 Reward
4. Results and analysis
5. Summary and future work
CONTENT

## Slide 13
3. Method description
Step 1: Data collection
Data (demand, PV supply, wholesale price)
Car usage survey
→car usage data
Technology parameter (charge/discharge speed limit, efficiency)
Step 2: Model construction
Generate agent
Design P2P energy trading model
Step 3: Train agents
Agent
Reward
…
…
…
State
Action
…

## Slide 14
1. Introduction and background
2. Objective
3. Methodology
3.1 Step 1: Data collection
3.1.1 Data (demand, PV supply, wholesale price)
3.1.2 Car usage survey → Car usage data
3.1.3 Technology parameter (battery charge/discharge speed limit, efficiency)
3.2 Step 2: Model construction
3.2.1 Generate agent
3.2.2 Design P2P energy trading model
3.3 Step 3: Train agents
3.3.1 Q table
3.3.2 Reward
4. Results and analysis
5. Summary and future work
CONTENT

## Slide 15
3.1.1 Data
 | Consumption | PV production | Wholesale electricity price
Location | UC Barkley (California) | California (For each zipcode) | California (For each zone)
Number of columns | 62 (93) Columns with more than 10% missing values are discarded, and the remaining columns are linearly interpolated. Data columns with average value of more than 30 [Wh/m^2*h] and less than 1 [Wh/m^2*h] are discarded. | 267 | 1 (4) Price data from Pacific Gas & Electric is selected.
Year | 2016/1/1~2017/12/31 | 2011/1/1~2016/12/31 | 2016/1/1~
Source | [1] | [2] | [3]
Histogram (average) |  |  | 
[1] https://www.kaggle.com/code/claytonmiller/building-data-genome-project-2-overview/data
[2] https://www.californiadgstats.ca.gov/downloads/
[3] https://www.caiso.com/Pages/default.aspx
Consumption [Wh/m^2 per hour]
Production [kWh/kW per hour]
Price [cents/kWh]

## Slide 16
3.1.2 Car usage survey → car usage data
Annual mileage [km/year] | Usage frequency | Ratio [%]
~ 3000 | Do not ride often | 12.9
3000 ~ 5000 | Mostly for nearby shopping | 25.8
5000 ~ 7000 | Mostly for commuting to work or school (approx. 30 min/one way) | 22.5
7000 ~ 9000 | Mostly used on weekends, sometimes trips | 14.8
9000 ~ 11000 | Mostly for commuting to work or school (approx. 60 min/one way) | 13.8
11000 ~ 16000 | Long drive every day | 6.0
16000 ~ | Super long drive | 4.2
Car usage survey [1]
[1] https://from.sonysonpo.co.jp/topics/pr/2023/07/20230727_01.html
1000 car usage profile are made according to the distribution of the car usage frequency

## Slide 17
3.1.3 Technology parameter
Parameter | Value
Battery charge efficiency [-] | 0.9
Battery discharge efficiency [-] | 0.9
EV battery charge efficiency [-] | 0.9
EV battery discharge efficiency [-] | 0.9
EV efficiency [km/kWh] | 7
Max battery charge speed [kW] | 3.0
Max battery discharge speed [kW] | 3.0
Max EV charge speed [kW] | 6.0
Max EV discharge speed [kW] | 3.0

## Slide 18
1. Introduction and background
2. Objective
3. Methodology
3.1 Step 1: Data collection
3.1.1 Data (demand, PV supply, wholesale price)
3.1.2 Car usage survey → Car usage data
3.1.3 Technology parameter (battery charge/discharge speed limit, efficiency)
3.2 Step 2: Model construction
3.2.1 Generate agent
3.2.2 Design P2P energy trading model
3.3 Step 3: Train agents
3.3.1 Q table
3.3.2 Reward
4. Results and analysis
5. Summary and future work
CONTENT

## Slide 19
3.2.1 Generate prosumer (agent)
Parameter | Value
Demand Response (DR) | True, False
DR shift limit [h] | 6.0, 12.0, 18.0, or 24.0
Elastic ratio [-] | off-peak: 0.5, mid-peak: 0.3, on-peak: 0.1※
Battery capacity [kWh] | 0 or 13.5
EV battery capacity [kWh] | 0 or 40
PV install capacity [kW] | 0 or 5
Car speed [km/h] | 30
Alpha | 1, 1.5, 2, 2.5, 3, 3.5, or 4
Beta | 1, 1.5, or 2
Gamma | 1, 1.5, 2, 2.5, 3, 3.5, or 4
Epsilon | 1, 1.5, or 2
Psi | 1, 1.5, 2, 2.5, 3, 3.5, or 4
Omega | 1, 1.5, or 2
※22PM-6AM: off-peak, 7AM-16PM: mid-peak, 17PM-21PM: on-peak
Demand, PV Supply, Car usage data are randomly chosen for each agent.
Other parameters for each agent are showed in the table
Described in 3.3.2 reward

## Slide 20
3.2.2 Design P2P energy trading model
Inelastic load
Battery
PV
Prosumer #3
Inelastic load
Elastic load
EV
Prosumer #4
Inelastic load
Elastic load
Battery
EV
PV
Prosumer #1
Inelastic load
Elastic load
EV
PV
Prosumer #2
Bid
Bid
Bid
Bid
Price, Amount2
Price, Amount4
Price, Amount1
Price, Amount3
Wholesale electricity market
&
independent system operator
Grid import
Grid export

## Slide 21
3.2.2 Design P2P energy trading model
Parameter | Value
Bid price max [cents/kWh] | 120
Bid price min [cents/kWh] | 10
Wheeling charge [cents/kWh] | 10
Sell price to grid [cents/kWh] | 0
Trade frequency [h] | 1
Number of agent [-] | 100

## Slide 22
3.2.2 Design P2P energy trading model
 | : | Net consumption
 | : | Inelastic consumption
 | : | Elastic consumption (Demand Response)
 | : | Shifted consumption from past DR
 | : | Battery charge/discharge (positive value for charging)
 | : | EV battery charge/discharge (positive value for charging)
 | : | Production from PV panel
 | : | Net consumption
 | : | Inelastic consumption
 | : | Elastic consumption (Demand Response)
 | : | Shifted consumption from past DR
 | : | Battery charge/discharge (positive value for charging)
 | : | EV battery charge/discharge (positive value for charging)
 | : | Production from PV panel
Net demands of each agent are defined as following equation:

## Slide 23
3.2.2 Design P2P energy trading model
 | : | Bid price for inelastic consumption
 | : | Upper bound of bid price
 | : | Bid price for inelastic consumption
 | : | Upper bound of bid price
 | : | Desired elastic consumption amount
 | : | Bid price for elastic consumption
 | : | Desired elastic consumption amount
 | : | Bid price for elastic consumption
One of the target of RL

## Slide 24
3.2.2 Design P2P energy trading model
 | : | Bid price at timeslot for shifted demand from timeslot
 | : | Lower bound of bid price
 | : | Patience period of DR
 | : | 
 | : | Lower bound of bid price
 | : | Patience period of DR

## Slide 25
3.2.2 Design P2P energy trading model
 | : | State of charge of battery[-]
 | : | Charging efficiency of battery
 | : | Discharging efficiency of battery
 | : | Battery capacity of battery
 | : | State of charge of battery[-]
 | : | Charging efficiency of battery
 | : | Discharging efficiency of battery
 | : | Battery capacity of battery

## Slide 26
3.2.2 Design P2P energy trading model
 | : | Binary decision variable whether EV is connected to the grid
 | : | State of charge of EV[-]
 | : | Charging efficiency of EV
 | : | Discharging efficiency of EV
 | : | Consumption of EV battery for mobility
 | : | Binary decision variable whether EV is connected to the grid
 | : | State of charge of EV[-]
 | : | Charging efficiency of EV
 | : | Discharging efficiency of EV
 | : | Consumption of EV battery for mobility

## Slide 27
1. Introduction and background
2. Objective
3. Methodology
3.1 Step 1: Data collection
3.1.1 Data (demand, PV supply, wholesale price)
3.1.2 Car usage survey → Car usage data
3.1.3 Technology parameter (battery charge/discharge speed limit, efficiency)
3.2 Step 2: Model construction
3.2.1 Generate agent
3.2.2 Design P2P energy trading model
3.3 Step 3: Train agents
3.3.1 Q table
3.3.2 Reward
4. Results and analysis
5. Summary and future work
CONTENT

## Slide 28
target：bid price for DR bid price buy/sell of battery/EV battery,
3.3 Train agents Learning method: Multi Agent Q Reinforcement Learning (Q-MARL)
 | : | The state at time and the set of all possible states
 | : | The action at time and the set of all possible actions
 | : | Estimated optimal action-value function
 | : | TD error
 | : | Policy
 | : | Learning rate
 | : | Discount rate
 | : | 
 | : | 
 | : | Estimated optimal action-value function
 | : | TD error
 | : | Policy
 | : | Learning rate
 | : | Discount rate
Learning parameter | Value
Learning rate | 0.99
Discount rate | 0.01
Episode | 100
Number of environment | 16

## Slide 29
Parameter | 
PV ratio [kW/kWh] | Digitized into 20 steps
Battery SOC [-] | Digitized into 20 steps
Parameter | 
PV ratio [kW/kWh] | Digitized into 20 steps
Battery SOC [-] | Digitized into 20 steps
Parameter | 
PV ratio [kW/kWh] | Digitized into 20 steps
Elastic ratio [-] | 0.1, 0.3, or 0.5 -> 3 steps
Parameter | 
PV ratio [kW/kWh] | Digitized into 20 steps
Elastic ratio [-] | 0.1, 0.3, or 0.5 -> 3 steps
3.3.1 Q table
DR
Battery buy
Number of column is possible bid prices (price_max – price_min) +1 = (120 - 10) +1 = 111
DR q table size = 20*3 × 111
= 60 × 111
Battery buy q table size = 20*20 × 111
= 400 × 11
Number of column is possible bid prices (price_max – price_min) +1 = (120 - 10) +1 = 111
Q tables are made for each agent individually.
Battery sell
EV Battery buy
EV Battery sell

## Slide 30
Parameter | 
PV ratio [kW/kWh] | Digitized into 20 steps
Parameter | 
PV ratio [kW/kWh] | Digitized into 20 steps
3.3.1 Q table
PV
Number of column is possible bid prices (price_max – price_min) +1 = (120 - 10) +1 = 111
PV q table size = 20 × 111
Q tables are made for each agent individually.

## Slide 31
3.3.2 Reward
 | : | Reward of agent at timeslot
 | : | Sell price to grid
 | : | Buy price from grid
 | : | Sell price in microgrid
 | : | Buy price in microgrid
 | : | Dissatisfaction value by DR
 | : | Dissatisfaction value by battery
 | : | Dissatisfaction value by EV battery
 | : | 
 | : | Sell price to grid
 | : | Buy price from grid
 | : | Sell price in microgrid
 | : | Buy price in microgrid
 | : | Dissatisfaction value by DR
 | : | Dissatisfaction value by battery
 | : | Dissatisfaction value by EV battery

## Slide 32
3.3.2 Reward
, | : | Coefficients of dissatisfaction value by DR
, | : | Coefficients of dissatisfaction value by battery
, | : | Coefficients of dissatisfaction value by EV battery
 | : | Coefficients of dissatisfaction value by DR
 | : | Coefficients of dissatisfaction value by battery
 | : | Coefficients of dissatisfaction value by EV battery

## Slide 33
Test simulation (Only exploitation, not update Q) is conducted every 10 episodes.

## Slide 34
1. Introduction and background
2. Objective
3. Methodology
3.1 Step 1: Data collection
3.1.1 Data (demand, PV supply, wholesale price)
3.1.2 Car usage survey → Car usage data
3.1.3 Technology parameter (battery charge/discharge speed limit, efficiency)
3.2 Step 2: Model construction
3.2.1 Generate agent
3.2.2 Design P2P energy trading model
3.3 Step 3: Train agents
3.3.1 Q table
3.3.2 Reward
4. Results and analysis
5. Summary and future work
CONTENT

## Slide 35
Result

## Slide 36
Result

## Slide 37
Result
Cents/kWh
kWh
Energy mix in microgrid (sum) @thread 0 @episode 20 (test)
SoC [%]

## Slide 38
Result

## Slide 39
Result

## Slide 40
Result

## Slide 41
Result
※BTW, the average grid price of electricity is 0.30 [$/kWh]

## Slide 42
1. Introduction and background
2. Objective
3. Methodology
3.1 Step 1: Data collection
3.1.1 Data (demand, PV supply, wholesale price)
3.1.2 Car usage survey → Car usage data
3.1.3 Technology parameter (battery charge/discharge speed limit, efficiency)
3.2 Step 2: Model construction
3.2.1 Generate agent
3.2.2 Design P2P energy trading model
3.3 Step 3: Train agents
3.3.1 Q table
3.3.2 Reward
4. Results and analysis
5. Summary and future work
CONTENT

## Slide 43
An autonomous decentralized energy system by using bidding is proposed.
Existence of PV panel may increase the volatility of unit cost of electricity.
Existence of Battery / EV may bring positive effect when they combined with DR.
In the presented simulation, the best facility combination is install only PV.
More agents (number of environment) may be required to smoothing out randomness.
Future tasks to do:
Construct the other model: Prosumers without P2P energy trading.
An assessment of impact against grid is required.
Summary and future work

## Slide 44
Summary and future work
Oct.
Nov.
Dec.
Mar.
Jan.
Feb.
2024
予備審査 エネコン前刷
健康診断
本審査
Construct a model without P2P trade
Analyze & Compare scenarios
秋合宿
Improve (Buffer)
Write thesis
Write paper

## Slide 45
Appendix

## Slide 46
CAPEX of PV
[1] https://www.nrel.gov/docs/fy22osti/83586.pdf
MMP model is used in the cost calculation.
CAPEX per year is calculated by Straight Line Method. The statutory useful life of the depreciable assets for PV is 17 years.
MSP: Minimum Sustainable Price
MMP: Modeled Market Price

## Slide 47
OPEX of PV
[1] https://www.nrel.gov/docs/fy22osti/83586.pdf
MMP residential model is used in the cost calculation.

## Slide 48
CAPEX of Battery
[1] https://www.nrel.gov/docs/fy22osti/83586.pdf
MSP: Minimum Sustainable Price
MMP: Modeled Market Price
MMP model is used in the cost calculation.
CAPEX per year is calculated by Straight Line Method. The statutory useful life of the depreciable assets for Battery is 6 years.
※OPEX of Battery is not provided in the NREL report.

## Slide 49
Previous research
Target variable | Method | Demand response | Battery | EV battery | bids | Year | Ref.
Energy retail price | Reinforcement Learning (Q-learning) | ✓ | - | - | - | 2018 | 1
Energy retail price | Deep Reinforcement Learning (Proximal Policy Optimization) | ✓ | ✓ | - | - | 2024 | 2
Energy retail price | Reinforcement Learning (Q-learning) | ✓ | ✓(Cen-tralized) | - | - | 2021 | 3
Total cost | Mixed-Lnteger Linear Problem | ✓ | ✓ | - | ✓ | 2020 | 4
Cost of each agent | Reinforcement Learning (DA-MADDPG) | - | ✓ | - | ✓ | 2021 | 5
Cost of each agent | Deep Reinforcement Learning (TD3) | - | ✓ | - | ✓ | 2023 | 6
[1] Renzhi Lu, Seung Ho Hong, Xiongfeng Zhang, "A Dynamic pricing demand response algorithm for smart grid: Reinforcement learning approach, " in Applied Energy, Vol. 220, pp. 220-230, 2018, doi: 10.1016/j.apenergy.2018.03.072.
[2] D. Watari, I. Taniguchi and T. Onoye, "Duck Curve Aware Dynamic Pricing and Battery Scheduling Strategy Using Reinforcement Learning," in IEEE Transactions on Smart Grid, Vol. 15(1), pp. 457-471, 2024, doi: 10.1109/TSG.2023.3288355.
[3] Li He, Yuanzhi Liu, Jie Zhang, “Peer-to-peer energy sharing with battery storage: Energy pawn in the smart grid,” in Applied Energy, Vol. 297, 117129, 2021, doi.org/10.1016/j.apenergy.2021.117129.
[4] Suyang Zhou, Fenghua Zou, Zhi Wu, Wei Gu, Qiteng Hong, Campbell Booth, “A smart community energy management scheme considering user dominated demand side response and P2P trading,” in International Journal of Electrical Power & Energy Systems, Vol. 114, 105378, 2020, doi.org/10.1016/j.ijepes.2019.105378.
[5] Qiu D., Wang J., Wang J., Strbac G,“Multi-Agent Reinforcement Learning for Automated Peer-to-Peer Energy Trading in Double-Side Auction Market,” in IJCAI International Joint Conference on Artificial Intelligence, pp. 2913 - 2920, 2021, doi.org/10.24963/ijcai.2021/401
[6] H. Zhang, K. Kok and N. G. Paterakis, "Deep Reinforcement Learning-Based Prosumer Aggregation Bidding Strategy in a Hierarchical Local Electricity Market," 2023 Asia Meeting on Environment and Electrical Engineering (EEE-AM), Hanoi, Vietnam, 2023, pp. 01-06, doi: 10.1109/EEE-AM58328.2023.10395533.

## Slide 50
Match frequency in present society (Japan)​
[1] OCCTO電力広域的運営推進機関, (参考資料)需給調整市場について (2019)

## Slide 51
背景 電力市場の自由化とP2P電力取引
従来の事業体制
各地域の一般電気事業者
発電
送電
配電
小売
消費者
供給義務、地域独占
総括原価方式による料金規制
電力システム改革後(2016年～)
発電
送配電
事業者
小売
法的
分離
←
(旧)一般電気事業者
発電
事業者
発電
事業者
発電
事業者
卸売電力取引市場 (JEPX)
小売電気
事業者
小売電気
事業者
小売電気
事業者
小売電力市場
生産
消費者
消費者
FIT
FIT
FIP
生産
消費者
生産
消費者
FIP
一般財団法人 新エネルギー財団 電力市場の概要(その1)